11B Analysis with S455 Setup
Setup and Detectors
Particle Identification
 12C(p,2p)11B reaction
Further Methods of Identification
Tobias Jenegger
R3B WG Meeting
11. Jan. 2021
Supported by BMBF 05P15WOFNA and 05P19WOFN1.
The results presented here are based on the experiment s444/s473, which was performed at the beam line/infrastructure Cave C at the GSI Helmholtzzentrum für Schwerionenforschung, Darmstadt (Germany) in the frame of FAIR Phase-0.
Physics with R3B
CALIFA – Design
TUM Members:
Roman Gernhäuser,Lukas Ponnath,Philipp Klenze,Tobias Jenegger

---
The S455 Setup (February 2020)
GLAD magnet
CALIFA
NeuLAND
R³B Music
MWPC1
neutrons
beam
MWPC0
START
MWPC2
TWIM Music
MWPC3
Daughter
nuclei
Beam energy: from 400 to 800 AMeV
Intensities: 1kHz - 1MHz
Beamtype: 12C,
Target: C, CH2
Time of Flight Wall

---
Particle Identification
START
TWIM Music
x
size*1.5{B %rho = {{%beta %gamma M} over {q}}}
MWPC1
MWPC0
z
Time of Flight Measurement: Start to TOFW
Flight-path Reconstruction: Tracking Detectors (MWPC1, 2 and 3)
Charge Measurement : TWIM Music
CALIFA
MWPC2
MWPC3
Time of Flight Wall
11B Analysis with S455 Setup

---
R3B @ FAIR
Flightpath Reconstruction
Radius Reconstruction:
size*1.5 {R = {L_eff} over {2sin({%theta_"in" + %theta_out} over {2}) } }
Known:
position and inflight angle (θin) before GLAD
position after GLAD (MWPC3)
color blue size*1.5 %theta_{ "in" }
     compute θout iteratively:
MWPC1
MWPC2
MWPC3

---
Charge versus A/q
12C
11C
10B
11B

---
12C(p,2p)11B reaction
p_1( vec p_1 , E_1 )
p( vec p_0 , E_0 )
p( vec p_A, E_a )
p_{A-1}( vec p_{A-1}, E_{A-1} )
p_A + p_T = p_1 + p_2 + p_{A-1} + p_{ %gamma }
p_{%gamma}( vec p_%gamma , E_%gamma )
p_2( vec p _{2} , E_2 )

---
Gamma Spectrum of 11B
Doppler Correction
size*2 E_{ %gamma } = size*2 %gamma size*2E_{ lab} size*2( 1- %beta cos (%theta ))
Single events can have multiple gamma hits
All gamma hits are filled into the histogramm (not just the hit with highest energy)
2.1 MeV (1/2-) p-hole state
5.0 MeV (5/2-) p-hole state

---
12C(p,2p)11B Analysis:
Beam energy: 400 AMeV
Beamtype: 12C
Beam Time: 3 hours
Target: CH2 (12.29mm)
Tracking Detectors: MWPC 1,2,3
ToF measurement: START to ToFW
Charge measurement: TWIM Music
Event selection criteria CALIFA:
→ two hits with Ehit > 30 MeV
11B level scheme:
2.1 MeV (½ -) p-hole state of 11B
Tobias Jenegger
11B Analysis with S455 Setup, Feb. 2020

---
Polar Angular Distribution of protons for 12C(p,2p)11B
12C beam
Barrel region with high acceptance
iPhos region
11B Analysis with S455 Setup

---
Arzimuthal Distribution of protons for 12C(p,2p)11B
z
x
y
Psi1 [degreees]
CALIFA left half (90°) iPhos
CALIFA right half (45°) iPhos
11B Analysis with S455 Setup
Tobias Jenegger
Psi2 [degreees]

---
Momentum Distribution 2p & 11B
expected: barrier line
Smearing ??
Methods for Investigation:
→ Simulation
→ Boosting to the 12C frame
→ CALIFA shifting / geometric validation
→ Background analysis

---
Simulation of the 12C(p,2p)11B reaction
Data:
Long. Mom p1p2 vs long. Mom. 11B

---
Simulation of Polar Angular Distribution
Simulation
Data
Theta1 plus Theta2 [degrees]
cut at ≈ 84 °
No. of Events

---
Polar and Arzimuthal Cuts
Polar cut: (p1+p2) < 84°
Arzimuthal cut: 180° +- 30° angular difference
size*2 %angle
with cut

---
Boosting to 12C Frame
size *1.5 p_{ 12C } + size *1.5p_{tr} = size*1.5 p_{ 1 } + size*1.5 p_{ 2 } + size*1.5 p_{11B}
size *1.5 p_{ 12C } = size*1.5 p_{ i } + size*1.5 p_{11B}
size *1.5 p_{ i } = size*1.5 p_{ 1 } + size*1.5 p_{ 2 } - size*1.5 p_{tr}
pi
11B
cos( %gamma ) approx -1
size*1.5%gamma
y
p1
green: using the arzimuthal angle of the crystal center
blue: sweeping +- 2.5° around the crystal center
→ sweep should also be done with polar angle
x
p2

---
Background Analysis
With 5.4 mm carbon target:

---
Summary & Outlook
→ Particle Identification works out
→ Gamma spectrum and angular distribution plots look reasonable
→ Further investigations for momenta distributions of the outgoing particles needed
→ Expand analysis towards 10B isotope
11B Analysis with S455 Setup
Tobias Jenegger

---
Thank you!
CALIFA @ Technical University of Munich (TUM)
Roman Gernhäuser, Lukas Ponnath, Philipp Klenze, Tobias Jenegger
Thank you!

---
Backup